Architectural and engineering specifications

N10KTV

• The 2-way full range passive loudspeaker system shall have one direct radiating 10-inch low frequency transducer and one 1,4-inch voice coil diameter, PETP diaphragm ferrite magnet compression driver loaded onto an asymmetrical rotational horn. Low frequency transducer shall be rated at a nominal impedance of 8 ohms. High frequency transducer shall be rated at a nominal impedance of 8 ohms.

• The usable bandwidth shall be 74Hz to 20kHz (-10dB).

• The system’s horizontal coverage shall be 50º to 100º, with vertical coverage of 55º.

• SPL, measured at 1W and 1m under free field conditions shall be 96 dB. Maximum SPL continuous, measured at 1m under free field conditions shall be 124 dB. Maximum SPL peak, measured at 1m under free field conditions shall be 127 dB.

• Maximum continuous musical program shall be 700W.

• Enclosure shall be bass-reflex type with two round ducts.

• Enclosure cabinet construction shall consist of birch plywood. Dimensions shall be 340 mm (13,4 inch) wide, 570 mm (22,4 inch) high, 365 mm (14,4 inch) deep. Enclosure weight shall be 18,7 Kg.

• Enclosure cabinet finish shall consist of black matt high-resistance Polyurea® paint.

• The front enclosure shall be protected by a 2mm steel grille with acoustically transparent technical mesh. The grille shall be secured via screws to keep it in place when facing the cabinet downwards.

• The enclosure shall include M8 points and internal hardware for rigging and shall be used in conjunction with dedicated rigging accessories. Rigging accessories shall be affixed with special crop resistant screws.

• The cabinet shall feature a 35mm (1,38 inch) diameter pole mount socket mounted on the bottom side, for a standard tripod.

• Electrical connections shall be made via one of the two 4-pole NL4MPR Speakon connectors with the following configuration: +1/-1 signal input, +2/-2 disconnected.

• The system shall include an internal passive crossover.

• The loudspeaker system shall be the Amate Audio® NITID N10KTV.

• The rigging accessories shall be the Amate Audio® ACR-M8, U-BL, HR-S, HR-S/GT.